## Slide 1
Arlington avenue traffic calming
March 07, 2022
Traffic Bureau

## Slide 2
Arlington Ave Project Timeline
September 2020: traffic calming request received
January 2021: traffic volume and speed data collected
April 2021: engineering evaluation performed, project accepted into design
July 2021: design phase paused for outreach with emergency services
February 2022: design phase restarted
March 2022: anticipated design complete
May 2022: begin construction

## Slide 3
Evolution of Traffic Calming Program

## Slide 4
Evolution of Traffic Calming Program
Lessons Learned:
Line striping and signage alone has minimal impact on speeding
Speed humps (and other vertical deflection devices) most effective at reducing 85% speeds above 25 mph
Uses of street extremely important when programming speed humps:
  Extra care needed on transit and emergency services routes
  Cannot deploy speed humps along entire street

## Slide 5
Arlington Ave Traffic Speed and Volume Data
Arlington west of Spring St
2021
  Average Daily Traffic: 4,000 vpd
  Median Speed: 30 mph
  85th Percentile Speed: 34 mph
  Percent of Motorists Driving
  over the Speed Limit: 82%

## Slide 6
Arlington Ave Traffic Speed and Volume Data
Arlington east of Spring St
2021
  Average Daily Traffic: 2,000 vpd
  Median Speed: 25 mph
  85th Percentile Speed: 32 mph
  Percent of Motorists Driving
  over the Speed Limit: 49%

## Slide 7
Arlington Ave Crash Data
Date range: 2016-2020
Limits: Frederick Street to Clover Street

## Slide 8
Early Action Improvements
Fernleaf All-Way Stop
All-way stop previously approved
Eastbound stop sign was not installed due to grade of street
Numerous community complaints to add sign
Traffic volumes roughly equivalent (meets warrant)
Installed on trial basis

## Slide 9
Potential Improvements
Preliminary Traffic Calming Plan
Intersection Daylighting
  Improve visibility by restricting parking at corners
Crosswalk Improvement
  Upgrade existing crosswalks to hi-viz markings
Centerline Removal
  Street too narrow if parking remains
Speed Control
  Speed Table or Speed Cushion, to be determined

## Slide 10
Potential Improvements
Speed Control
Primary emergency service and transit route
  Cannot construct speed humps in series along entire length of Arlington
  Need for alternate type of speed hump that supports services
Speed Table Speed Cushion